## Slide 1: REVIT LIBRARIES AND COLLECTIONS
Built around you.
TIPS FOR DOWNLOADING & USING REVIT FILES
Notes: 3D symbols are available for Marvin, Integrity, and Infinity.

## Slide 2: MARVIN.COM
Finding the ZIP file on the TECHNICAL SPECIFICATIONS page:
    Select a tab at the top for Windows, Doors, Skylights or Spaces
    Select the desired product’s “Collection/Product Line” (Signature Ultimate field is a drop-down box) at the left
    Click on the Product’s drop-down box to select the product
    Select Drawings as the default Documents will only be PDF files. Use the drop-down below it to narrow the files down to Revit
  A link to the Technical Specifications is now found on each product page

## Slide 3: Download and Extract the Compressed ZIP
The file listings contains library and collection files
  Library files contain every door and/or window Revit family available for a product collection or product line
    If you are using more than one type of product in a project, it could be a time saver downloading these files
    The ZIP file contains folders for each product category
  Collection files contain all the Revit families available for a certain product type
    The Ultimate Awning, for example, contains not only the standard awning but an awning assembly file as well as Awning Narrow Frame and Push Out
  Besides the RFA files the ZIP file will most likely contain TXT files that contain standard sizes for each RFA
    It is important to keep the TXT file in the same location on your computer as the RFA file to access this listing
Click on the file to download and select Save when prompted to save the file to your Downloads folder
In your Downloads folder, right-click the file and select “Extract All…”
Browse to the file location you would like to save the files, such as your Revit library or Desktop to be moved to your Revit library at a later time

## Slide 4: Assembly Families
The Library and Collection files contain some assembly families to speed up the design process but please use these with caution:

## Slide 5: Loading a Family
It is important to load the family from your open Revit project in order to access the standard sizes located in the text file
In the Load Family dialog box, click on the product you would like to add from your library and click the Open button in the lower right…

## Slide 6: Loading a Family continued…
Navigate to the folder and select the RFA file you would like to load
  The Preview at the right is a handy way to determine a shape if you are looking at a specialty shape folder
Click Open and select the Type you need…
  Holding down the Ctrl button allows you to select more than one size
  If the RFA you selected you selected does not have a TXT file associated with it, this is because that particular product does not have a standard size listing and is ordered by custom sizes only

## Slide 7: Working in Your Project
Once the product has been loaded to your project, it will be located in the Project Browser in the Doors or Windows categories. Double-click the Type to customize that product in the Type Properties dialog box or drag and drop it into a wall, highlight it and Edit Type from the Properties screen
Examples:
  Lite cut
  Finishes
  Glazing
  Operation
  Casing
  Sill type

## Slide 8: Changing Configuration…
Typically, you can change the product’s configuration once it is loaded into your project. The Ultimate Bi-Fold Door will need to have the correct number of panels selected when you are loading it into your project. You will not be able to switch from an 8 panel door to a 7 panel door, for example, by editing the type. You will be able to switch that 7 Panel door from a 4L3R_3L4R to a 7L0R_0L7R, however, from the Type Properties Construction category. Each configuration option is listed with a Option number associated with it and at the end of the listing, you can enter that Option number to change the configuration. Toggling the arrows in plan will switch direction the door is operating

## Slide 9: Changing Lite Cut
The standard divided lite for this particular door is 3W5H Rectangle cut but you could:
  Deselect Muntin Visibility in the Graphics category
  Change amount wide and/or high
  Shown is the Prairie 9 option… The width and height of the corners are adjustable.

## Slide 10: Material Families
  The Signature Ultimate line and the Elevate and Essential Collections have separate Materials files for the exterior color options
    Loading these files into your project will give you access to them from within the door or window family

## Slide 11: Save Time with Modern Detail Families
With our newest product line, we had the opportunity to add native Revit detail families
  They are found in the Details folder in all Modern compressed ZIP file
  These Section and Plan 2D families would be loaded to your project the same way as the door or window family but will be added to the Detail Items category
  They are easily placed over the standard family when you are working on Construction Detailing
  Parameters can be adjusted to match the standard family

## Slide 12: To Contact Us…
Can’t find the product you need? Or, maybe you need further assistance working with our files?
E-mail BIMsupport@marvin.com
Or, call 1-800-472-8895
We appreciate hearing your feedback and new model development requests